## Slide 1: Bakken Simulation Tutorial
Construct, run, visualize
Last Updated: July, 2025

## Slide 2: Premise
This is a step-by-step tutorial.
  The first phase is setting up and running a simple simulation.
  The second phase is visualizing the simulation results using ResFrac’s 3D viz tool.
The accompanying excel sheet contains all the data you need to input during the tutorial <Bakken_training_input_data_06-06-2025.xlsx>
  Tabs are laid out with descriptive names for the data they contain

## Slide 3: Phase 1: Model setup

## Slide 4: Phase 1 Overview
Step through each panel:
  Welcome
  Startup
  Static Model
  Curve Sets
  Wells and Perforations
  Meshing Options
  Fluid Model Options
  Fracture Options
  Proppants
  Water Solutes
  Well Controls
  Output Options
The following internal wizards are used:
  Properties versus depth wizard
  Wellbore survey import wizard
  Vertical mesh alignment tool
  Black oil wizard
  Water solutes wizard
  Production sequence wizard
Objective: Set-up a single-well Middle Bakken (MB) model (injection and production) using the data provided.
A Three Forks (TF) well is included as a placeholder for future history matching and optimization [not included here].

## Slide 5: Open ResFrac
Find (or search for) the ResFracPro App and open.
Make sure you have downloaded and installed the ResFrac Pro App and have an active license.

## Slide 6: Login to ResFrac
If prompted, log in.

## Slide 7: Create file path for new simulation (slide 1 of 2)
Create new project

## Slide 8: Create file path for new simulation (slide 2 of 2)
Create new Sandbox workflow

## Slide 9: Create simulation from Bakken template
Create Sim

## Slide 10: Welcome panel: No modifications necessary
Read the ‘Note on Item Visibility’ and watch the 3-minute tutorial to get oriented.

## Slide 11: Startup Panel: No modifications necessary
Visibility of parameters on the start-up panel is controlled by the Advanced Options panel. The default visibility settings are template specific, and thus may not match this screenshot.

## Slide 12: Static model: Fluid pressure initialization method
Change to ‘Specify pressure gradient by layer’

## Slide 13: Static model: import formation properties (slide 1 of 4)
Select the ‘Properties versus depth wizard’.
Enter the number of properties to import, and the target layer thickness (used for upscaling).
Fill in the ‘Enforced Layer Boundaries’ table, which will define facies depths. This data can be copied from the ‘Geo data’ tab in the excel file and pasted into the table (create ‘New Row’ first).
Option to import from file shown in later slides

## Slide 14: Static model: import formation properties (slide 2 of 4)
Tip: enter your properties in the wizard in the same order as the columns for your input data
Properties may be found by scrolling or typing.
Note: If vertical Young’s Modulus (YM) is not specified, YM will be isotropic by default.

## Slide 15: Static model: import formation properties (slide 3 of 4)
Create a new row
Copy the properties from the ‘Geo data’ tab in the excel file and paste them into the table.

## Slide 16: Static model: import formation properties (slide 4 of 4)
Choose which properties to use to determine layer boundaries during upscaling
Click ‘Apply’ to create your new static model (auto populates the ‘Geological Units’ table)

## Slide 17: Static model: import formation properties from file (slide 1 of 6)
An alternative option in the ‘Properties versus depth wizard’ is to import the static model data directly from an LAS file (as opposed to manual entry, i.e. copy and paste from the spreadsheet).

## Slide 18: Static model: import formation properties from file (slide 2 of 6)
Enter your properties in the wizard based on the columns from the LAS file (excluding depth).
Properties may be found by scrolling or typing.
Note: If vertical Young’s Modulus (YM) is not specified, YM will be isotropic by default.
*Check that the units match those in the builder. If not, there will be the option to apply a conversion factor later.

## Slide 19: Static model: import formation properties from file (slide 3 of 6)
Select LAS file to import

## Slide 20: Static model: import formation properties from file (slide 4 of 6)
Map LAS file curves to static model table. Apply unit conversion factors if necessary.
Scroll and cont.

## Slide 21: Static model: import formation properties from file (slide 5 of 6)
Verify table imported correctly.
(Row adjustment options above not needed here)

## Slide 22: Static model: import formation properties from file (slide 6 of 6)
Choose which properties to use to determine layer boundaries during upscaling
Click ‘Apply’ to create your new static model (auto populates the ‘Geological Units’ table)
This step is the same as with the manual property import:

## Slide 23: Static model: Geological Units table, upscaling
Note how the data was upscaled:

## Slide 24: Static model: Geological Units table, reorder columns
Columns can be reordered by selecting the column header. Once your cursor becomes a hand icon, you can click and drag the columns to the desired location.
Prior to the next step, drag the “Show in viz tool” and the “Curve set” columns to the left next to depth columns.

## Slide 25: Static model: Geological Units table, facies visibility
You can scroll down the layers and find the facies names that were input into the wizard. These layers have automatically been marked to “Show in viz tool”.

## Slide 26: Curve sets: delete unnecessary curve sets
Switch to the Curve sets panel. The template has five curve sets created by default. Only two curve sets are listed in the excel file: Pay and Non-pay. Keep two of the five curve sets that can represent Pay and Non-pay, delete the rest.

## Slide 27: Curve sets: rename remaining two curve sets
Rename to match the listed curve sets in the excel file: Pay and Non-pay

## Slide 28: Static model: Geological Units table, assign curve sets (slide 1 of 2)
Return to the Static Model panel and assign the newly named curve sets to the corresponding layers in the Geological Units table, based on the excel file assignments.
(for tips on this step, see next slide)
Excel file data:
Curve set column may need to be moved closer to the Name column.

## Slide 29: Static model: Geological Units table, assign curve sets (slide 2 of 2)
Tips:
Click the top cell under ‘Curve set name’ and select Non-pay. Right-click, ‘fill down’.
Assign the Middle Bakken layer to ‘Pay’
Grab the green square in the lower right corner of the cell, and drag down to all layers between the Middle and Lower Bakken.
Repeat for the Three Forks Pay

## Slide 30: Static model: Geological Units table, modulus anisotropy & embedment
Set modulus anisotropy to 0.8 and proppant embedment to 0.02. Assign the top cells, right click and ‘fill down’ to assign a constant value for all layers.

## Slide 31: Static model: change SHmax azimuth
Set SHmax direction to 42 degrees.

## Slide 32: Curve sets: set PDP using PDP wizard
Return to the Curve Sets panel and select the ‘Pressure dependent permeability wizard’. It will automatically set the permeability enhancement for each curve set based on the assigned layers.
*Apply the wizard to all layers

## Slide 33: Curve sets: Check the PDP tables
The resulting PDP tables can be found by expanding each curve set, scrolling down to the ‘Reversible pressure dependent permeability table’ section, and viewing the ‘Isotropic permeability factor’ tables.
.
.
.
scroll
.
.
.
scroll

## Slide 34: Wells and perfs: delete wells from template
Delete default wells

## Slide 35: Wells and perfs: import wells from surveys (slide 1 of 4)
Important: when importing the first well, re-center the matrix around 14,400 MD. This is the center of the well section to be simulated.
Enter wellbore info (included in the excel sheet, Well data tab, Well_MB1) into wellbore survey import wizard.

## Slide 36: Wells and perfs: import wells from surveys (slide 2 of 4)
Copy the well survey data (for Well_MB1) from the excel sheet into the wizard

## Slide 37: Wells and perfs: import wells from surveys (slide 3 of 4)
Important: when importing the second well, do not re-center the matrix. That would override the matrix location, which was already centered around the first well.
Repeat for second well - Enter wellbore info (included in the excel sheet, Well data tab, Well_TF1)

## Slide 38: Wells and perfs: import wells from surveys (slide 4 of 4)
Repeat for second well - Copy the well survey data (for Well_TF1) from the excel sheet into the wizard
Note: Best practice is to clear the pre-existing table prior to pasting in a new table, to avoid residual rows from the previous dataset.

## Slide 39: Wells and perfs: view well positions
Select the 3D model icon to preview the wells
*This view has Facies visibility turned on, and 3x vertical stretch.

## Slide 40: Wells and perfs: adjust landing zone of wells (slide 1 of 2)
Adjusting the landing zone depth shifts the wellbore up or down so that the wellbore intersects the correct layer in the matrix. This is used to correct for formation dip, which isn’t accounted for in the ‘Geological Units’ table.
Note: the Middle Bakken spans from the layer named “Middle Bakken” (layer 25) through layer 32. To land the well approximately in the center of the Middle Bakken, select layer 29 as the landing zone.
Adjust the matrix region depth for the first well. This re-centers the mesh vertically around the new landing zone.

## Slide 41: Wells and perfs: adjust landing zone of wells (slide 2 of 2)
Repeat for second well (Well_TF1).
Note: the Three Forks spans from the layer named “Three Forks Pay” (layer 35) through layer 40. To land the well approximately in the center of the Three Forks, select layer 38 as the landing zone.
Do not adjust the matrix region depth for the second well. This will override the recentering around the MB1 well.

## Slide 42: Wells and perfs: recheck well positions
Select the 3D model icon to preview the wells
*This view has Facies visibility turned on, and 3x vertical stretch.
*Note that the toe depths of the wells have been shifted.

## Slide 43: Wells and perfs: add stages
We will be simulating a single stage, so the MD distance in the model is set to be the same as the stage length.
No need to make new matrix region center (already recentered in the previous steps)

## Slide 44: Wells and perfs: expand well details and add clusters
.
.
.
Expand each well, and scroll down to define the stage data (from the Well data tab in the excel file)
Stage length / cluster spacing = clusters per stage
scroll
.
.
.
scroll
300 ft/30 ft = 10
300 ft/25 ft = 12
Excel file data:

## Slide 45: Wells and perfs: add external fractures
External fractures are used to “mimic” the stress shadow of previously completed stages that are not included in the section model
Convention is to place an external fracture at 0.5*{cluster spacing} outside the matrix
Settings do not need to be exact; however, adding something ‘representative’ here goes a long way in preserving realism. Optionally, this can be done iteratively by running the sim once to get representative fracture properties, then using those as external fracture inputs for a second run.
Assign either fracture distance from the edge of the matrix, or (x,y,z) coordinates of the fracture.
Assign either net pressure or fracture volume. Net pressure used in this example.

## Slide 46: Wells and perfs: check perforations in 3D image
Open 3D preview
Use “matrix slices” option at the bottom of the screen to hide upper layers (I “viewed” layers 1 - 12 for this image)
Hover over visibility toggles (green sliders at bottom of screen), and turn “Perforations” on
Check that MB1 has 10 clusters and TF1 has 12 clusters. 10x horizontal stretch was used here to make perforations more identifiable.
This image is viewed from above (by selecting the “Z” display in the upper right corner)

## Slide 47: Meshing options: vertical mesh alignment wizard
Switch to the Meshing Options panel, and scroll down to the Vertical mesh alignment tool
This tool aligns the vertical mesh with the layers in the static model.
Align the matrix mesh from 10,000 to 10,600 ft (this should be approximately centered around the MB1 well)

## Slide 48: Fluid model: use black oil wizard
Switch to the Fluid Model Options panel. Use the Black oil wizard to create a black oil table, using data in the excel sheet, Fluid test tab.
Excel file data:

## Slide 49: Fracture options: No modifications necessary
This panel is primarily used during calibration efforts to modify the behavior of fracture propagation
During model setup, the default values here are sufficient so no changes are necessary

## Slide 50: Proppants: add 100 mesh proppant
Switch to the Proppants panel, then add 100 mesh proppant.
Right-click on the row # and duplicate the 40/70 White
Update name and diameter of new proppant

## Slide 51: Proppants: add 100 mesh to mixtures list
This new row represents a proppant mixture containing 100% 100 mesh proppant.
All proppants must be put into a mixture for use in the injection sequence (even if the mixture only contains one proppant type).

## Slide 52: Proppants: conductivity loss
Enter time-dependent proppant conductivity loss parameters for the new proppant

## Slide 53: Water solutes: add slickwater (slide 1 of 4)
Switch to the Water Solutes panel, then add FR (friction reducer) as a water solute.
Right-click on the row # and duplicate HVFR
Update name of new fluid

## Slide 54: Water solutes: add slickwater (slide 2 of 4)
3. Create a new mixture called ‘slickwater’ and make the mass fraction of FR non-zero.
Note: The water solutes wizard (next step) will adjust the viscosity multiplier of the FR water solute (based on the mass fraction) to achieve the desired viscosity of the slickwater mixture. 0.001 is recommended.

## Slide 55: Water solutes: add slickwater (slide 3 of 4)
Use the water solutes wizard to adjust the properties of FR to mimic slickwater

## Slide 56: Water solutes: add slickwater (slide 4 of 4)
Observe that ‘slickwater’ viscosities now look like slickwater

## Slide 57: Well controls: add MB1 injection sequence (slide 1 of 3)
Switch to the Well Controls panel
Click “Add Block” to add new wellbore controls

## Slide 58: Well controls: add MB1 injection sequence (slide 2 of 3)
2. Change “Shut in” to “InjectionSequence”

## Slide 59: Well controls: add MB1 injection sequence (slide 3 of 3)
Change injection units to “massPerSlurryVolume” and “SlurryRate”
Input injection controls (from excel file, tab Stimulation design)
Note: set max injection pressure to something arbitrarily high. The sim will consequently be rate controlled. We want to control injection rate, then will history match to treating pressures.
Note: last step has a rate of 0 bpm. This gives time for the ISIP to be calculated.

## Slide 60: Well controls: add MB1 shut-in after fracturing
Hint: use an “IsolateWell” shut-in type for improved simulation performance

## Slide 61: Well controls: add MB1 production sequence (slide 1 of 2)

## Slide 62: Well controls: add MB1 production sequence (slide 2 of 2)
Enter data from the excel file (Production history tab) into the Production table in the Production sequence wizard.
Include all data for plotting purposes.
These options relate to plotting the data inputs along with the simulation outputs.

## Slide 63: Well controls: check that production sequence added in correct location
Primary production type defaults to LiquidPlusGasRate.
Choose secondary production type - it should be something reliable.
Help icons (?) contain more info.
Production Sequence is correctly located after shut-in

## Slide 64: Output Options: check that additional line plots were added
Supplemental data is calculated from the raw input data (cumulative production, GOR, etc.)
Scroll to the ‘Additional Line Plots’ section of the Output Options panel - it should have auto-populated from the Production Sequence Wizard table data. If not, check your wizard inputs. This data can be plotted alongside simulation results in the viz tool.
Check that all properties entered into the Production Sequence Wizard are included.
Keep scrolling to see full table

## Slide 65: Well controls: max simulation time
By default, the production wizard leaves the final duration in the production sequence blank. These boundary conditions will consequently be applied for the remainder of the simulation. This is recommended.
Set the maximum simulation time to 5 years (43,800 hrs).

## Slide 66: Well controls: set TF1 to isolate well
Switch to editing Well_TF1
“Add Block”
Change Shut-in type to IsolateWell
If no Duration is specified, the block goes into effect for the rest of the simulation.

## Slide 67: Output options: add VFR and frac hit trackers
Switch to the Output options panel, scroll down, and turn on Volume to first response (VFR) and Frac hit trackers.
Set Well_MW1 as the injection well
Set Well_TF1 as the observation well

## Slide 68: Output options: Stress observation plane
Including a horizontal stress observation plane allows the mechanical stress to be viewed in the viz tool. This can be used to depict the stress shadow.
Additional columns
These inputs represent the extents of the stress observation plane, and the number of data points (observations) to record.

## Slide 69: Output options: economic model
Add new economic model and fill in based on the spreadsheet. Apply to both wells.
Cont.
Cont.
Anything parameters not included in the spreadsheet can be left as their defaults.

## Slide 70: Output options: add extra fracture info
.
.
.
scroll
Should already be checked in the Bakken template

## Slide 71: Save and Exit Builder
When saving the sim, all Errors and Warnings will be summarized. Any Errors need to be corrected prior to running the sim. The warnings should be reviewed but may not need to be addressed. The sim will still run.

## Slide 72: Run Simulation (slide 1 of 2)
Click on the simulation name, or the ellipses on the right, and select “Run Simulation” from the list of actions.

## Slide 73: Run Simulation (slide 2 of 2)
Click on the simulation name, or the ellipses on the right, and select “Run Simulation” from the list of actions.
Use most recent simulator version (default).
Choose job priority and Vm size depending on speed with which you want results (defaults are fine).
Then wait for simulation to run.

## Slide 74: Phase 2: Viz Tool

## Slide 75: Phase 2 Overview
Line plot 1
  Injection rate
  WHP
  BHP
  Proppant concentration
  Efficiency
Line Plot 2
  Cumulative oil
  GOR
  Water Cut
Objective: Use the 3D viz tool to visualize the Bakken tutorial simulation and analyze the results.
3D Images to plot (and questions to answer)
  Any view of fractures
    Fracture height and length
    Cluster efficiency
  Pressure
    Pressure distribution after production
  Proppant concentration
    Where did the proppant go?
    How does it correspond to conductivity?
  Fracture conductivity
    How does it correspond with proppant and stress?
  Effective Normal Stress
    How does it change over time?
    How does is correspond to conductivity?
  Cumulative oil production
    Which layer(s) produce the most oil?
    How does is correspond to pressure depletion?

## Slide 76: Visualize Simulation Results
Once the simulation run is complete and results downloaded, select “Visualize Simulation Results” from the list of actions.
Click on the simulation name, or the ellipses on the right, to pull up action options

## Slide 77: Viz Tool: Default View
By default, the results of the simulation will show one line plot and three 3D plots.

## Slide 78: Viz Tool: Panel Grid (slide 1 of 3)
Select “Panel Grid” at the bottom of the Viz tool to change the plots types and number of plots.
Select the ellipses (…) to expand options

## Slide 79: Viz Tool: Panel Grid (slide 2 of 3)
Choose plot type or add additional plots (panels).
3D panels with matching camera groups display the same angle and zoom

## Slide 80: Viz Tool: Panel Grid (slide 3 of 3)
To analyze this data, we will display two line plots and enable two additional panels, for a total of six active panels.

## Slide 81: Viz Tool: Selecting parameters to plot
Choose what each plot is showing via the gear icon (line plot), or by choosing a new displayed parameter (3D plot)

## Slide 82: Viz Tool: Line Plot 1, Injection data (Well_MB1)
Select the gear icon for the first line plot. Enter a title and choose data to plot. The data may share an axis (and scale) or be on a different axis.
On Axis 1, plot: WHP, BHP
On Axis 2, plot: Proppant concentration (prop mass/vol)
“Add new Axis”
On Axis 3, plot: Water inj rate
“Add new Axis”
On Axis 4, plot: Efficiency
Type or scroll to find parameters.
Watch out for abbreviations.
Clear axis to remove all currently plotted parameters.
scroll

## Slide 83: Viz Tool: Line Plot 1, Injection data (Well_MB1) - zoom
Expand first panel, then zoom into the injection period. See tips on how below.
Resize panels
Change scale by clicking + dragging, or clicking + typing
Slide scale by clicking + dragging
Zoom by clicking + dragging on the plot (either direction, or both).
Reset scale by double-clicking on plot.
Can scale each axis individually

## Slide 84: Viz Tool: Line Plot 1, Injection data (Well_MB1) - zoom
Hover over the plots to see data values

## Slide 85: Viz Tool: Line Plot 2, Production data (Well_MB1)
Repeat process with Line Plot 2. Select the gear icon for the second line plot. Enter a title and choose data to plot.
On Axis 1, plot: Cumulative Oil Production (Oil tot prod)
On Axis 2, plot: Instantaneous GOR
“Add new Axis”
On Axis 3, plot: Water cut (instantaneous and cumulative)
scroll

## Slide 86: Viz Tool: Line Plot 2, Production data (Well_MB1) - zoom
Expand second panel. It will show the full production period by default.

## Slide 87: Viz Tool: Line Plot 2, Production data (Well_MB1) – historical data
The actual production data can also be plotted alongside the simulated results. The data was automatically added to the output options (additional line plots) when using the production sequence wizard. Consequently, we can return straight to the gear icon menu.
On Axis 1, add: Cumulative Oil Production, Ext
On Axis 2, add: Instantaneous add, Ext
On Axis 3, plot: Water cut, Ext (instantaneous and cumulative)
The historical data is labeled as external (Ext), so you can type “ext” to search for available plots.

## Slide 88: Viz Tool: Line Plot 2, Production data (Well_MB1) – historical data view
Note the deviation between the simulated results and historical data. This is a base sim that still needs to be history matched.
You may need to change the vertical scale to see the full dataset
You can change the line colors (or make dashed lines) in the gear menu

## Slide 89: Viz Tool: Line Plot 2 – Manage Line Plot Data Sets
If historical data wasn’t included in the output options during the simulation, you can alternatively import a csv.
To correctly format the csv file, it is recommended you copy the sim track file, remove unwanted columns, and paste in new data.
The only currently loaded data file is the sim track for the current simulation.

## Slide 90: Viz Tool: 3D plots, navigation
3D Control tips are available in the viz tool via the (?) icon. Changing timesteps can be done using the bottom right menu.
Clicking the “Time / Snapshot” button opens new menu to navigate 3D views through time. Default is end of sim.
The (?) button is in the upper left corner of each 3D panel. All panels in the same camera group are adjusted simultaneously.

## Slide 91: Viz Tool: 3D plots, parameter selection
Assign the 3D panels as the following: 1. Pressure, 2. Proppant total mass per area, 3. Fracture Conductivity, 4. Effective normal stress. Later we’ll also look at 5. Cumulative net oil production per area.
To reassign 3D panel parameters, click on the current parameter, and start typing the name of the parameter. Keep in mind, some may be abbreviated.

## Slide 92: Viz Tool: 3D plots, fracture view
To just view the fractures, turn off the Matrix Visibility using the toggle at the bottom of the screen. This visibility setting applies to all 3D panels by default. However, this can be applied to individual panels using 3D Panel Controls.

## Slide 93: Viz Tool: 3D plots, fracture dimensions
Under “Show Value with Click,” toggle the “Calculate Distance” tool to measure the length and height of the fractures.
Click on two points to measure the distance between them.
Fracture length:
Fracture height:

## Slide 94: Viz Tool: 3D plots, stretch view
To more easily view individual fractures, apply a 10x horizontal stretch.
Note, “Calculate Distance” does not work with rotated stretch on.

## Slide 95: Viz Tool: 3D plots, cluster efficiency
Click on “Visibility” to see additional visibility options. Toggle on “Perforations” to compare number of fractures to perforations.
Count: 10 fractures formed, & 10 perfs

## Slide 96: Viz Tool: Proppant and Conductivity (5 yrs)
View the proppant and conductivity panels (which should be next to each other), and rescale the color bar.
Update max values
Observations:
Proppant area directly corresponds to fracture conductivity
Compare to effective stress over time (next slides)

## Slide 97: Viz Tool: Proppant, Conductivity, and Stress over time
Choose which timesteps to view. The terminal BHP is reached after 0.7 yrs (see line plot). Use this as a benchmark to compare properties over time. Then compare this to an early time (~30 days, 0.1 yrs) and a late time (5 yrs, end of sim).
Double click to scale this plot back to full extents to find the terminal BHP.

## Slide 98: Viz Tool: Proppant, Conductivity, and Stress over time (0.1, 0.7, 5 yrs)
Cycle through timesteps (0.1, 0.7, and 5 yrs), and compare the proppant, conductivity, and stress distributions over time.
Observations:
Proppant area stays the same over time.
As effective normal stress increases over time, fracture conductivity decreases.
Time dependent conductivity decline contributes between 0.7 and 5 yrs.
0.1 yrs
0.7 yrs
5 yrs
Change timestep here
Proppant
Conductivity
Stress

## Slide 99: Viz Tool: Pressure plot
Expand the 3D pressure panel, and rescale the color bar.
Click on the max value to change scale – type desired value. Set the max pressure approximately equal to the reservoir pressure, ~7000 psi.
Observations:
Medium pressure gradient after 5 yrs (~200 ft of low pressure around the wellbore)
Some areas are being drawn down very effectively
Combination fracture and matrix limiting
Compare to oil production (next slide)

## Slide 100: Viz Tool: Compare Pressure plot to Cumulative Oil Production
Below the pressure panel, change the shown parameter from “Effective normal stress” to “Cumulative net oil production per area”. Then you can view pressure and cum oil production together. Expand both windows and zoom to a reasonable level. These can also be compared to conductivity distribution.
Observations:
Area of most pressure depletion generally corresponds to greatest oil production.
Depleted area also corresponds to propped conductivity.

## Slide 101: Viz Tool: Oil Production
Turn on the facies visibility, and use vertical and horizontal stretch to view which layer(s) produce the most oil.
Observations:
Most of the oil production is focused in the Middle Bakken.
Vertically offset fractures suggest stress shadowing effects.
Settings:
Toggle facies visibility on.
30x horizontal stretch applied, and 6x vertical stretch.

## Slide 102: Viz Tool: Additional Outputs – VFR and frac hit trackers (Line Plot 1)
You can show Volume to First Response (VFR) and frac hits on the injection plot.
On Axis 2, add: Frac hit counter
“Remove” Axis 4
“Add new Axis”
On Axis 4, plot: VFR

## Slide 103: Viz Tool: Additional Outputs – VFR and frac hit trackers (Line Plot 1)
You can show Volume to First Response (VFR) and frac hits on the injection plot.

## Slide 104: Viz Tool: Additional Outputs – Extra fracture info (Line Plot 1)
Here we can use the injection plot as a base.
“Remove” Axis 2-4
On Axis 2, add any frac info of interest. In this case, we selected the height and length of the fracture.
You can also show extra fracture information, which splits results up by each fracture or perforation.
Search for “Frac” to see available plots.

## Slide 105: Viz Tool: Additional Outputs – Extra fracture info (Line Plot 1)
Here we see the fracture growing during stimulation. Frac by frac Production parameters could also be shown on Plot 2.

## Slide 106: Viz Tool: Additional Outputs – Economics model (Line Plot 3)
“Remove”/ “Clear” Axes
Choose any econ models of interest. Here we put DROI and Instantaneous IRR on Axis 1.
Add a third line plot panel.
Search for “Econ” to see available plots.

## Slide 107: Viz Tool: Additional Outputs – Economics model (Line Plot 3)

## Slide 108: Viz Tool: Additional Outputs – Stress Observation Planes (slide 1 of 2)
In one of the 3D panes, switch the parameter to Delta stress in the Shmin direction. Rotate view and turn on external fracture visibility.

## Slide 109: Viz Tool: Additional Outputs – Stress Observation Planes (slide 2 of 2)
You can now view stress shadowing over time. There is initial stress shadowing from the external fractures, then additional stress is introduced during stimulation, which then dissipates and stabilizes over time.
1 hr
5 yrs
0 hr
3 hr
External fractures

## Slide 110: Phase 2 Conclusions
Simulated production is about half of the actual.
Fracture size is ~ 1850 ft x 250 ft.
Stress shadowing has caused fractures to be vertically offset from each other.
The propped area corresponds to the region of highest fracture conductivity
High fracture conductivity also corresponds to the region of highest pressure depletion and oil production.
Fracture conductivity decreases over time as a result of increasing effective normal stress, as well as time dependent effects.
There is a medium pressure gradient, indicative of a mixture of fracture and matrix limiting conditions.

## Slide 111: Thank you!
Chris Ponners, Reservoir and Completions User Success Lead
cponners@resfrac.com
Aileen Zebrowski, Reservoir and Completions Engineer
aileen@resfrac.com