## Slide 1
ResApps: StageOpt
Key Physics

## Slide 2: Even with high perf pressure drop, what prevents perfect uniformity?

## Slide 3: Initial hole size and phasing are not uniform; then, proppant erosion is uneven, worsening uniformity over time

## Slide 4: Effect of phasing on initial hole size
A correlation can be used to predict the effect of phasing on initial diameter.
This effect can be tuned up or down to match field observations.

## Slide 5: Effect of gravity and phasing
Degree of gravitational settling captured with the dimensionless number “G”.
The calculation also accounts for the difference in gun angle and wellbore angle, because the gun sits towards the bottom of the hole.

## Slide 6: Effect of inertia and phasing
Some particles miss a perforation due to higher density than fluid.
“Missed” proppant temporarily elevates concentration locally nearby perforation azimuth.
Downstream perforations receive elevated proppant due to increase in local concentration.
Effect is shown in CFD simulations (Liu et al. (2021) and Wang et al. (2022)) and observed in field data.

## Slide 7
ResApps: StageOpt
History Match Cheat Sheet

## Slide 8: History Matching Parameters
Group | Parameter | Effect
Perforation Erosion | Erosion alpha multiplier | Controls the rate of erosion from flow through a perforation; increase to increase the amount of erosion everywhere
 | Erosion gamma multiplier | Controls the rate of erosion from flow past a perforation; increase to increase the amount of heel bias
 | Nugget/Sill/Range for erosion alpha | Creates spatially correlated variance in erosion alpha; increase to reduce erosion uniformity index and widen error bars in erosion charts. (Rule of thumb: Set range to stage length. Set nugget to 20% of sill. Vary nugget and sill up and down to match UI.)
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile
 | Stress shadow | Represents the residual stress shadow from the previous stage; increase to increase the magnitude of heel bias
 | Effective tensile strength/uncertainty | The amount that pressure must exceed local minimum principal stress for a perf to initiate; use tensile strength to match breakdown pressures and tensile strength uncertainty to match perforation (non)initiation.
 | Near wellbore tortuosity (NWT) coefficient and exponent | Excess pressure drop in the near wellbore region (between clusters and fractures); use to match stepdown tests. Higher NWT smooths out erosion variability and trends along the stage.
Perforation parameters | Prob of perf plugging multiplier | Modifies the built-in correlation to determine if a perforation plugs during a stage; increase to increase the frequency of plugging
Other physics options | Inline correction multiplier | Modifies inertial calculations to account increased erosion downstream for inline perforations in a cluster; increase to increase erosion/proppant in downstream perforations.
 | Suspension multiplier | Modifies the gravitational settling of proppant to account differing proppant types. Finer meshes require higher values than coarser meshes. A higher value results in less settling.
Most important matching parameters
Parameters changed less-frequently

## Slide 9: Erosion alpha multiplier
Heel
Flow
Increasing Erosion of perf
Alpha set to zero – no erosion
As Alpha increases erosion increases uniformly
Toe
Group | Parameter | Effect
Perforation Erosion | Erosion alpha multiplier | Controls the rate of erosion from flow through a perforation; increase to increase the amount of erosion everywhere

## Slide 10: Erosion alpha multiplier - Example
Erosion Alpha Multiplier = 0.2
Erosion Alpha Multiplier = 0.8

## Slide 11: Erosion gamma multiplier
Heel
Flow
Increasing Erosion of perf
Gamma set to zero – no lateral velocity erosion effect
As Gamma increases so does preferential heel erosion
Toe
Group | Parameter | Effect
Perforation Erosion | Erosion gamma multiplier | Controls the rate of erosion from flow past a perforation; increase to increase the amount of heel bias

## Slide 12: Erosion gamma multiplier - Example
Erosion Gamma Multiplier = 0
Erosion Gamma Multiplier = 1

## Slide 13: Nugget/Sill/Range for erosion alpha
Group | Parameter | Effect
Perforation Erosion | Nugget/Sill/Range for erosion alpha | Creates spatially correlated variance in erosion alpha; increase to reduce erosion uniformity index and widen error bars in erosion charts.
The nugget and sill multipliers act to create a lognormal distribution variance in the erosion alpha for each perforation.
Reasonable ranges appear to be between 0.05-0.4.
Rule of thumb:
  Set range = stage length.
  Set sill to be 20% greater than the nugget.
  Vary nugget and sill up and down to best match UI after matching the overall trend (heel/toe bias).

## Slide 14: Nugget/Sill/Range for erosion alpha Interlude - Stage-to-stage variance
Perf imaging results for erosion can be highly variable from stage to stage
Perforation Number
Final Perforation Diameter
Trellised by Stage

## Slide 15: Nugget/Sill/Range for erosion alpha Interlude - Erosion variance and impact on uniformity
Known Input Variance:
  Cluster spacing variance
  Perforation phasing variance
  Initial perf diameter variance
Unknown Input Variance:
  Breakdown pressure
  Erosion coefficients
Potential causes for variance in erosion:
  Variability in steel quality or stress state
  Quality of cement behind casing
  Local variability in formation properties and/or transverse fractures immediately behind casing
  Positive feedback loop

## Slide 16: Nugget/Sill/Range for erosion alpha Interlude – Example model with inline perforation
Perforation Number
Realization #
Perforation Number
Uncertainty in shot diameter, perf phasing
Realization #
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
1 | 0.30018 | 0.31779 | 0.27617 | 0.24773 | 0.25772 | 0.24565 | 0.24388 | 0.22914 | 0.23099 | 0.2328 | 0.2256 | 0.22471 | 0.27145 | 0.24387 | 0.26238 | 0.20945
2 | 0.28175 | 0.27527 | 0.26898 | 0.26859 | 0.23634 | 0.2284 | 0.22955 | 0.22965 | 0.21975 | 0.21972 | 0.23132 | 0.228 | 0.20945 | 0.25711 | 0.25738 | 0.23287
3 | 0.33491 | 0.30169 | 0.32098 | 0.27977 | 0.26162 | 0.25276 | 0.25098 | 0.24662 | 0.23909 | 0.24381 | 0.24522 | 0.25372 | 0.24053 | 0.25876 | 0.30365 | 0.26389
4 | 0.28131 | 0.28656 | 0.27818 | 0.23565 | 0.26217 | 0.24748 | 0.24491 | 0.22619 | 0.22522 | 0.22057 | 0.22312 | 0.23385 | 0.23748 | 0.26028 | 0.25141 | 0.21147
5 | 0.30013 | 0.28906 | 0.28355 | 0.27326 | 0.25268 | 0.24591 | 0.25935 | 0.25806 | 0.24102 | 0.22872 | 0.24322 | 0.23253 | 0.23576 | 0.22774 | 0.25463 | 0.24534
6 | 0.3006 | 0.26406 | 0.25489 | 0.25936 | 0.24556 | 0.22232 | 0.2113 | 0.21441 | 0.19577 | 0.20015 | 0.22471 | 0.22332 | 0.23575 | 0.22097 | 0.29362 | 0.21531
7 | 0.32949 | 0.32229 | 0.29939 | 0.28308 | 0.29663 | 0.26994 | 0.27896 | 0.24858 | 0.26175 | 0.27238 | 0.25498 | 0.25335 | 0.24998 | 0.26366 | 0.28997 | 0.28468
8 | 0.27135 | 0.27268 | 0.27251 | 0.25385 | 0.23584 | 0.23966 | 0.26061 | 0.22445 | 0.21443 | 0.21829 | 0.2149 | 0.24345 | 0.24574 | 0.22879 | 0.23679 | 0.20755
9 | 0.31973 | 0.29149 | 0.28661 | 0.28062 | 0.2761 | 0.24986 | 0.25472 | 0.26792 | 0.24768 | 0.24186 | 0.2395 | 0.2474 | 0.23376 | 0.26652 | 0.2761 | 0.29223
10 | 0.29306 | 0.2983 | 0.29948 | 0.28103 | 0.28405 | 0.25363 | 0.25101 | 0.24342 | 0.24894 | 0.24691 | 0.2715 | 0.25201 | 0.23286 | 0.28713 | 0.28626 | 0.31649
11 | 0.32314 | 0.30578 | 0.31815 | 0.27536 | 0.29695 | 0.26498 | 0.28267 | 0.25101 | 0.26374 | 0.24369 | 0.26014 | 0.24028 | 0.22875 | 0.23954 | 0.28691 | 0.26824
12 | 0.27835 | 0.30338 | 0.26723 | 0.26607 | 0.26234 | 0.2409 | 0.23348 | 0.23141 | 0.22295 | 0.22059 | 0.2402 | 0.22671 | 0.20773 | 0.22516 | 0.21935 | 0.24801
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
3 | 0.27209 | 0.36484 | 0.4448 | 0.18059 | 0.43013 | 0.25435 | 0.53582 | 0.39439 | 0.41068 | 0.4276 | 0.32957 | 0.39172 | 0.2083 | 0.44579 | 0.233 | 0.19299 | 0.17617
7 | 0.43544 | 0.35117 | 0.61529 | 0.24436 | 0.20808 | 0.32161 | 0.38644 | 0.34786 | 0.25503 | 0.17998 | 0.19512 | 0.1664 | 0.18875 | 0.22133 | 0.23413 | 0.21526 | 0.35078
11 | 0.23715 | 0.2426 | 0.46349 | 0.33461 | 0.21538 | 0.20956 | 0.16872 | 0.22668 | 0.21635 | 0.48414 | 0.17146 | 0.27696 | 0.33926 | 0.19427 | 0.47507 | 0.23665 | 0.27317
21 | 0.31844 | 0.3248 | 0.22828 | 0.20877 | 0.36301 | 0.15372 | 0.2565 | 0.29777 | 0.20647 | 0.26128 | 0.44551 | 0.25589 | 0.38398 | 0.29256 | 0.26607 | 0.1468 | 0.07858
40 | 0.26369 | 0.1768 | 0.26488 | 0.2838 | 0.27454 | 0.28823 | 0.20536 | 0.15503 | 0.19706 | 0.24274 | 0.21456 | 0.26623 | 0.15237 | 0.23784 | 0.16755 | 0.15818 | 0.065511
56 | 0.45686 | 0.27756 | 0.23141 | 0.19196 | 0.4496 | 0.17611 | 0.16297 | 0.33782 | 0.20145 | 0.15981 | 0.17044 | 0.1631 | 0.20653 | 0.25112 | 0.24374 | 0.27828 | 0.085063
80 | 0.27424 | 0.21514 | 0.27704 | 0.49556 | 0.20971 | 0.36366 | 0.66054 | 0.49889 | 0.27952 | 0.30808 | 0.2807 | 0.3977 | 0.20642 | 0.21009 | 0.34689 | 0.41119 | 0.28611
Final shot diameter
Uncertainty in shot diameter, perf phasing + spatially correlated erosion variance

## Slide 17: Nugget/Sill/Range for erosion alpha
Equivalent Diameter Increase (%)
Cluster + Perforation #
Field Model
The goal is to capture both the “average” trend behavior as well as the spread in erosion ranges and thus UI

## Slide 18: Fracture net pressure
Heel
Flow
Increasing Erosion of perf
Toe
Single Cluster Stress Shadow
Each frac generated in a cluster generates it’s own stress shadow
Perf/frac
Group | Parameter | Effect
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile

## Slide 19: Fracture net pressure
Less erosion in middle of cluster
Heel
Flow
Increasing Erosion of perf
Toe
Cumulative stress shadow from cluster fracs
Cumulative Stress Shadow
Group | Parameter | Effect
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile

## Slide 20: Fracture net pressure
Group | Parameter | Effect
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile
The effects of fracture net pressure are most strong when stage length is long or cluster spacing is tight.
The best calibration for net pressure can be achieved if there are multiple wells with similar designs, with the exception of either stage length or cluster spacing.
We would generally expect fracture net pressure to be less than the stress shadow (from the previous stage) at the toe.

## Slide 21: Stress shadow
Heel
Flow
Increasing Erosion of perf
Toe
Stress Shadow from previous frac
Previous Stage Frac Stress Shadow
Higher stress in the rock gives less erosion
Group | Parameter | Effect
Fracture and Reservoir | Stress shadow | Represents the residual stress shadow from the previous stage; increase to increase the magnitude of heel bias

## Slide 22: Stress shadow
Group | Parameter | Effect
Fracture and Reservoir | Stress shadow | Represents the residual stress shadow from the previous stage; increase to increase the magnitude of heel bias

## Slide 23: Combination of “Fracture net pressure” and “Stress shadow”
Heel
Flow
Increasing Erosion of perf
Toe
Combined Stress Shadow
U shaped erosion profile
Previous frac
This cluster
Combined stress shadow

## Slide 24: Effective tensile strength/uncertainty
Group | Parameter | Effect
Fracture and reservoir | Effective tensile strength/uncertainty | The amount that pressure must exceed local minimum principal stress for a perf to initiate; use tensile strength to match breakdown pressures and tensile strength uncertainty to match perforation (non)initiation.
Effective tensile strength increases the breakdown pressure.
Effective tensile strength uncertainty defines random cluster-by-cluster variability in that tensile strength depending on the distribution selected in the “Uncertainty” section (uniform or normal).
This uncertainty is useful to model when a significant percentage of clusters do not break down, even with substantial limited-entry pressure drop.

## Slide 25: Near wellbore tortuoisty (NWT) coefficient and exponent
Group | Parameter | Effect
Fracture and reservoir | Near wellbore tortuosity (NWT) coefficient and exponent | Excess pressure drop in the near wellbore region (between clusters and fractures); use to match stepdown tests. Higher NWT smooths out erosion variability and trends along the stage.
NWT is the excess pressure drop in the near-wellbore region between clusters and fractures.
History matching with real world examples has shown that it has a minor impact on erosion, so recommended values of 200psi/bpm^(1/2) and 0.5 are often reasonable.
If available, NWT can be calibrated from step-down tests.

## Slide 26: Prob of perf plugging multiplier
Group | Parameter | Effect
Perforation parameters | Prob of perf plugging multiplier | Modifies the built-in correlation to determine if a perforation plugs during a stage; increase to increase the frequency of plugging
Controls the tendency for shots to screen out in the near-wellbore region.
The model uses a probabilistic calculation proportional to the proppant mass flowing through a perforation.
Set to 0 to prevent any perf plugging.

## Slide 27: Recommended workflow for matching Erosion UI
Perform a detailed analysis of the available perf imaging data to determine the perf phasing uncertainty at the stage/cluster/perf level, the perforation diameter uncertainty, the phasing effect of perf diameter multiplier, and the cluster position uncertainty. Include these in the “Inputs” panel.
Set Nugget/Sill for erosion alpha = 0.
Match the trend over the stage with alpha, gamma, net pressure, stress shadow, and potentially others.
  This will show the component of uniformity loss that is due to systematic biases (e.g. heel bias, toe bias, etc.) as well as variance due to the natural completion uncertainties.
Set the Range for erosion alpha = stage length.
Slowly step up nugget and sill multipliers to match Erosion UI. We generally see the sill about 20% higher than the nugget.
  Viewing the overall distribution of perforation area such as in the CDF in the “Results”->”Summary” panel can be helpful as well.

## Slide 28
Christopher Ponners cponners@resfrac.com
Thank You