## Slide 1
ResApps
Key engineering and geoscience workflows in cutting-edge, practical, easy to use apps

## Slide 2: Agenda
What are ResApps?
Background on StageOpt
Demo User Interface Walkthrough
Example of History Matching and Optimization

## Slide 3: Why ResFrac exists
Our purpose is to help operators maximize rate of return – increase production, reduce cost, and reduce risk.
Direct – Calculate the optimal well spacing and frac design.
Indirect – Develop new insights and tools that provide the foundation for better decision making.
Pareto front

## Slide 4: ResFrac Pro
All physics are solved simultaneously in ResFrac for every time step!
Fracturing, leak-off, shut-in, and production without ever remeshing
Fracture properties, like conductivity and aperture, computed as a function of normal stress
Industry-leading proppant transport modeling and fracture realism
Fractures are true fractures with real aperture of millimeters
4

## Slide 5: What is the difference between ResFrac Pro and Resapps?
ResApps are smaller, focused tools that address specific problems and/or parts of the engineering workflow.
They can be used alongside ResFrac Pro, or independently.
ResFrac Pro simulations run on the server, and are managed from a locally installed user-interface.
ResApps are pure web apps, accessed from resapps.resfrac.com.

## Slide 6: The ResApps web portal

## Slide 7
StageOpt
Improve perforation design to optimize proppant placement

## Slide 8: The value of fracturing uniformity
Plug and perf completion has become ubiquitous in shale because perforation pressure drop can be used to overcome stress shadowing and force tight fracture spacing.
The uniformity of fluid and proppant placement has a direct effect on IP and EUR.
Kaufman et al. (2019)
8

## Slide 9: Downhole imaging
Downhole imaging gives us a relatively affordable, high-fidelity technology for measuring uniformity post-job.
This facilitates an engineering workflow – you make a change in perforation strategy, and then measure the outcome.
Iterate, measure, and improve!

## Slide 10: Uniformity Index
Uniformity index is used to quantify uniformity.
UI can be defined for erosion, final diameter, proppant flow, or slurry flow.
Can be defined on a per cluster or per shot basis.
Is sometimes ‘regularized’ for the number of clusters/shots.
Most often, UI is reported ‘per cluster’ for ‘erosion.’ But what actually matters is ‘per cluster’ for ‘proppant flow.’ These are not the same thing, but erosion is what we measure!
10

## Slide 11: Note that even with perfect uniformity of outflow, the far-field fractures are still not identical. Still, drainage becomes considerably more uniform.
11

## Slide 12: The ‘value of the perfect stage’ – seven figures per well

## Slide 13: StageOpt – a wellbore dynamics simulator
The proppant transport and erosion correlations are incorporated into a fast-running wellbore dynamics simulator.
Time-steps through the injection schedule, calculating distribution of flow and erosion in every timestep.
Must consider:
  Breakdown
  Perforation and NW pressure drop
  Stress shadowing (prior stage and within the stage)
  Random variance in phasing, diameter, and breakdown pressure (Monte Carlo)
  Proppant inertial and gravity effects
  Perforation erosion
  Effect of phasing on initial diameter
  Perf plugging
13

## Slide 14: What it takes to model proppant placement
z
14

## Slide 15: What it takes to model proppant placement
z
15

## Slide 16: The workflow
StageOpt has several ‘calibration’ knobs. Most importantly, the ‘alpha’ coefficient that determines the magnitude of erosion per lbs of proppant outflow.
Therefore, you need to calibrate. The workflow is:
  Gather downhole imaging data. Data has significant random variability from stage-to-stage; therefore, it is best to use just one design along an entire well, or only a few.
  Summarize the key statistical behaviors observed (heel/toe bias, overall amount of erosion, and any variability observed between different designs)
  With the calibrated model, run alternative scenarios to evaluate changes in: (a) phasing, (b) shot count per cluster, (c) initial hole diameter, (d) tapered perforating.
  Trial in the field and repeat the downhole imaging measurements.
  Evaluate performance and iterate.
You could do this without a simulator, but we can help find that best design faster. Help you propose a design that you might not have otherwise tested.
Roll out that design widely. If changing geology, proppant type, etc., consider more data collection and/or simulation to reoptimize.

## Slide 17: Eagle Ford case study
Unoriented 120’ phasing perforations – 3 shots per cluster (except two heel clusters had 2 shots).
180 ft stage length, 10 clusters per stage.
17

## Slide 18: Calibration results
In this case, proppant placement is more uniform than erosion.
Erosion related to lateral velocity. Heel biased erosion cause heel biased slurry flow. But this is countered by the inertial effects.
In this particular case, the effects cancel out and proppant is fairly uniform.
Operator had used fewer shots per cluster towards the heel, but this was unnecessary in this case and reduced uniformity per cluster.
18

## Slide 19: Sensitivity analysis on alternative perforation designs
The upper plot shows uniformity index as a function of perforation pressure drop. Interestingly, if there is too much limited entry, this harms uniformity. Erosion becomes very strong, and it occurs nonuniformly.
The lower plot shows three perf designs (the three colored bars) and different job sizes. In this comparison, the main conclusion was that the ‘light blue’ perf design is significantly worse.
Increasing strength of limited entry
19

## Slide 20
StageOpt Demo

## Slide 21: Modern, web-based, easy-to-use user-interface
21

## Slide 22
StageOpt
Worked Example

## Slide 23: The workflow
  Gather downhole imaging data. Data has significant random variability from stage-to-stage; therefore, it is best to use just one design along an entire well, or only a few.
    Plot % diameter increase as a function of perforation or cluster with a statistical distribution.
    Calculate the cluster-level erosion uniformity index (UI) for each stage and plot its distribution.
  Summarize the key statistical behaviors observed (heel/toe bias, overall amount of erosion, and any variability observed between different designs)
  Calibrate model
    Overall magnitude of erosion
    Specific trends over MD (heel bias, toe bias, heel/toe bias, neutral)
    Matching erosion variance and UI
  Test alternative designs by focusing on key sources of low uniformity

## Slide 24: Example Data Set – Selection from 35 stages
Entry Design:
  300 ft stage length
  8 clusters/stage with 3spf @ 60deg phasing (unoriented)
  1800 psi of limited entry
Completion design:
  45 bbl/ft; 4000 lb/ft
  Slickwater
  100M and 40/70M
Cluster Number (heel=left; tow=right)
Eroded Area (in^2)

## Slide 25: Aggregate Trends
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)
25

## Slide 26: Key History Match Observations
Observation | Target | Model Parameter
Erosion Magnitude | Average diameter increase of 71% | Erosion alpha
Stage Erosion Trends | Heel and toe clusters both have bias and erode 85%; middle of stage has reduced erosion, but it is asymmetric (lowest erosion in clusters 5/6) | Erosion gamma; stress shadow; fracture net pressure
Erosion Uniformity Index | Avg cluster level erosion UI of 0.4 with a STD of 0.26 | Trend match; Nugget/Sill/Range for erosion alpha
Cluster Level Erosion UI

## Slide 27: Key History Matching Parameters
Group | Parameter | Effect
Perforation Erosion | Erosion alpha multiplier | Controls the rate of erosion from flow through a perforation; increase to increase the amount of erosion everywhere
 | Erosion gamma multiplier | Controls the rate of erosion from flow past a perforation; increase to increase the amount of heel bias
 | Nugget/Sill/Range for erosion alpha | Creates spatially correlated variance in erosion alpha; increase to reduce erosion uniformity index and widen error bars in erosion charts. (Rule of thumb: Set range to stage length. Set nugget to 20% of sill. Vary nugget and sill up and down to match UI.)
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile
 | Stress shadow | Represents the residual stress shadow from the previous stage; increase to increase the magnitude of heel bias

## Slide 28: Initial Model Comparison
Model average diameter erosion of 57% vs goal of 71%
More heel bias needed in model.
Erosion UI of 0.75 vs goal of 0.4
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)

## Slide 29: StageOpt – iterating for a good history match
Heel
Flow
Increasing Erosion of perf
Alpha set to zero – no erosion
As Alpha increases erosion increases uniformly
Toe
Group | Parameter | Effect
Perforation Erosion | Erosion alpha multiplier | Controls the rate of erosion from flow through a perforation; increase to increase the amount of erosion everywhere
29

## Slide 30: Initial Model Comparison – Alpha 0.4 -> 0.6
Model average diameter erosion of 69% vs goal of 71%
More heel bias needed in model.
Erosion UI of 0.75 vs goal of 0.4
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)

## Slide 31: StageOpt – iterating for a good history match
Heel
Flow
Increasing Erosion of perf
Gamma set to zero – no lateral velocity erosion effect
As Gamma increases so does preferential heel erosion
Toe
Group | Parameter | Effect
Perforation Erosion | Erosion gamma multiplier | Controls the rate of erosion from flow past a perforation; increase to increase the amount of heel bias
31

## Slide 32: Initial Model Comparison – Gamma 0.1 -> 0.4
Model average diameter erosion of 73% vs goal of 71%
More heel bias present. Could use a bit more as well as lowing erosion in the middle.
Erosion UI of 0.75 vs goal of 0.4
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)

## Slide 33: Fracture net pressure
Less erosion in middle of cluster
Heel
Flow
Increasing Erosion of perf
Toe
Cumulative stress shadow from cluster fracs
Cumulative Stress Shadow
Group | Parameter | Effect
Fracture and Reservoir | Fracture net pressure | Represents the stress shadow that occurs during fracturing; increase to reduce erosion in the middle of the stage, i.e. create a heel and toe bias or “U”-shaped profile
33

## Slide 34: Initial Model Comparison – Net pressure 100psi -> 300psi
Model average diameter erosion of 72% vs goal of 71%
Heel and toe bias; “U”-shaped profile
Erosion UI of 0.68 vs goal of 0.4
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)

## Slide 35: Initial Model Comparison – Nugget/Sill 0x -> 0.15/0.2
Model average diameter erosion of 71% vs goal of 71%
Heel and toe bias; “U”-shaped profile
Erosion UI of 0.42 vs goal of 0.4
Cluster Number and Perforation (heel=left; tow=right)
Equivalent Diameter Increase (%)

## Slide 36: Final History Match

## Slide 37: Optimization

## Slide 38: Optimization Ideas
Based on studies so far, there is no single uniform recommendation for the ‘best perforation design.’
Depending on stage architecture, pump schedule, and local geologic factors, stages may tent towards heel bias, toe bias, heel/toe bias, or a neutral bias.
Design changes should be made to counteract history-matched and observed sources of low uniformity:
  To remove toe bias, consider:
    Inline perforations to mitigate inertial effects
    A phasing toward the top of the well
  To remove heel bias, consider:
    A tapered perforating scheme
    A lower pump rate
  To remove heel/toe bias, consider:
    A unique perforating scheme
    A shorter stage length
    A phasing toward the side or bottom of the well
  To remove cluster to cluster variance with a neutral trend, consider:
    A greater number of smaller perforations
    Increased limited entry
Increasing limited-entry perforation pressure drop (LE) can often help, but only to a certain point. Too much LE can result in excessive erosion, resulting in worse uniformity.
There is no single universally ‘best’ perforation phasing. Depends on circumstances.

## Slide 39: Example Optimization
Changes from history matched case:
  Moved from 60deg unoriented to top inline orientation
  Moved from 3spf to tapered perf design
  Increased limited entry from 1800 psi to 2400 psi
39

## Slide 40: Example Optimization
Changes from history matched case:
  Moved from 60deg unoriented to top inline orientation
  Moved from 3spf to tapered perf design
  Increased limited entry from 1800 psi to 2400 psi

## Slide 41: The ‘value of the perfect stage’ – seven figures per well
4% increase in IP365
$500,000 increase in NPV
Notes: 0.687->

## Slide 42: Modern, web-based, easy-to-use user-interface
42

## Slide 43: Relevant Papers

## Slide 44
Thank You